## Slide 1
Working of 7 Segment Display
7 Segment Display
Seven segment displays Actually has 7 because it has 7 LEDs in it. It also has a decimal point led on it.
Each LED can be made ON or OFF individually.
By making LEDs ON and OFF in different pattern makes different digits or characters on Display.
1
2
3
4
5
6
7
point
With 7 Segment Display we can make numbers from 0 to 9 and Alphabets from A to F.

## Slide 2
Pins of 7 Segment Display
7 Segment Display
8LEDs(including decimal point) on 7 segment display has the segments named a, b, c, d, e, f, g, and dp respectively.
The segment display can be divided into two types: common anode and common cathode segment displays, by internal connections.
For a common-anode LED, the common anode should be connected to the power supply (VCC); for a common-cathode LED, the common cathode should be connected to the ground (GND).
a
b
c
d
e
f
g
dp
gnd
gnd
a
b
f
g
dp
c
d
e

## Slide 3
Pins of 7 Segment Display
7 Segment Display
In each display there are LEDs segmented so we need resistor for protecting LEDs.
The segment display can be divided into two types: common anode and common cathode segment displays, by internal connections.
For a common-anode LED, the common anode should be connected to the power supply (VCC); for a common-cathode LED, the common cathode should be connected to the ground (GND).
a
b
c
d
e
f
g
dp
gnd
gnd
a
b
f
g
dp
c
d
e

## Slide 4
Pins of 4 Digit 7 Segment Display
4 Digit 7 Segment Display
The 4-digit segment display is a 4*8-shaped LED display device composed of 32 LEDs (including four decimal points). The segments arenamed respectively a, b, c, d, e, f, g, h, dig1, dig2, dig3, and dig4.
For a common-anode LED, the common anode should be connected to the power supply (VCC); for a common-cathode LED, the common cathode should be connected to the ground (GND).
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
dig1
a
f
dig2
dig3
b
dig4
g
c
dp
d
e

## Slide 5
Pins of 4 Digit 7 Segment Display
4 Digit 7 Segment Display
  The 4-digit segment display is a 4*8-shaped LED display device composed of 32 LEDs (including four decimal points). The segments arenamed respectively a, b, c, d, e, f, g, h, dig1, dig2, dig3, and dig4.
For a common-anode LED, the common anode should be connected to the power supply (VCC); for a common-cathode LED, the common cathode should be connected to the ground (GND).
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
a
b
c
d
e
f
g
dp
dig1
a
f
dig2
dig3
b
dig4
g
c
dp
d
e

## Slide 6
Arduino Uno
Ultrasonic
Sensor
Tank Pump
LCD
Screen
Soil Moisture
Sensor
GSM SIM900
Module
Relay module
Plant Water Pump
Relay module
Power Supply